## Slide 1
MANUFACTURING OPERATIONS & PLANNING
Whole-Factory Optimal Process Scheduling & Operations Framework
Unifying Make-vs-Buy Decisions, Flexible Job Shop Optimization, and Human-in-the-Loop Shop Floor Execution
PART I: IMPLEMENTED
Make vs Buy MILP + Baseline JSSP
PART II: IN-PLANNING
Flexible Job Shop + Cart Logistics
REALITY GROUNDING
No AGVs / No IoT: Human-in-the-Loop

## Slide 2
SYSTEM OVERVIEW
Executive Architecture: From Orders to Machine Execution
The Industrial Challenge & Local Optima
Siloed Decisions Fail: Deciding Make-vs-Buy purely on annual machine capacity creates unexecutable shop-floor blockages.
Physical Coupling: A CNC machine cannot cut without raw blanks wheeled from stores, tooling fixtures, and qualified machinists.
Bottleneck Propagation: If intermediate staging racks are full, upstream machines are physically blocked from unloading.
Factory Reality: Precision optical & CNC shops do not have multimillion-dollar AGVs or IoT streaming telemetry. Scheduling must work with manual carts and supervisor shift feedback.
Integrated Two-Pillar Framework
Pillar 1: Implemented Baseline (Code Active) • Order-Level Make vs Buy MILP (PuLP) • Multi-Criteria Decision Making (MCDM: Risk, Strategy, Finance) • Baseline CP-SAT Job Shop Scheduler • Streamlit Interactive Operations Dashboard
Pillar 2: In-Planning Target (Whole Factory) • Flexible Job Shop (Parallel CNC/Polishing Machine Pools) • Sequence-Dependent Setup Times (SDST Changeovers) • Inter-Bay Cart Transit & Staging Buffer Capacities • Vacuum Coating Batching & Thermal Curing Rules • Human-in-the-Loop Disruption Repair (Right-Shift & Re-Solve)

## Slide 3
PART I: WORK COMPLETED
Implemented: Make vs. Buy Multi-Criteria Optimizer
Mathematical Formulation
Solver Engine: PuLP Mixed-Integer Linear Programming (MILP).
Decision Variables: Integer Make_vars[i] and Buy_vars[i], linked by Binary IsMake[i].
Strict Demand Fulfill: Make[i] + Buy[i] == Order_Qty[i].
Capacity Handshake: Machine net capacity limits: Sum(Setup + Run * (1 + Scrap)) <= Available_Hours.
Critical Policy: Critical items strictly forbidden from external purchase (Buy[i] == 0).
4 Selectable MCDM Goals
💰 Financial Performance: Minimizes raw materials, direct labor, machine runtime costs, and vendor purchase prices.
🛡️ Sourcing Risk: Penalizes IP leakage, vendor financial instability, and supplier disruption risk (-8 to +8 scale).
👥 Managerial Performance: Optimizes transaction complexity, supplier relationship value, and customer perception.
🏆 Strategic Competitiveness: Penalizes external lead times and vendor defect rates while rewarding internal volume flexibility.
Interactive Deliverables
Order-Level Tagging: Categorizes orders automatically into MAKE, BUY, or MAKE & BUY.
Executive KPI Cards: Instant readouts for Total Units Made, Units Bought, Optimal Penalty Score, and Split Orders.
Decision Distribution: Interactive Plotly Pie and Bar charts visualizing volume splits.
Scenario Stress-Testing: Machine capacity slider (0.1x to 2.0x) to test bottleneck shocks.
Output File: Exports decisions directly to Final_Make_Buy_Decisions.csv for scheduling.

## Slide 4
PART I: WORK COMPLETED
Implemented: Baseline Job Shop Scheduler (CP-SAT)
Constraint Programming Formulation
Engine: Google OR-Tools CP-SAT (Constraint Programming with SAT solver).
Order Filtration: Pulls all orders where Make_In_House_Qty > 0 from Make/Buy decisions.
Task Duration Logic: Duration = Setup_Hours + (Run_Hours_Per_Unit * Qty). Formulated in integer minutes.
Machine Interval Variables: IntervalVar(start, duration, end) with AddNoOverlap across each machine's operations.
Job Precedence: Strict chain start_var(op_k+1) >= end_var(op_k).
Dual Objective Modes: Minimizes Total Makespan (C_max) OR Total Weighted Due-Date Tardiness (sum max(0, C_i - d_i)).
Factory Working Calendar & UI Visualization
Real Working Calendar Mapping: Maps integer solver minutes into 10-hour working days (8:00 AM - 6:00 PM), 6 days a week (Monday to Saturday, Sundays closed).
Interactive Multi-Track Gantt: Visualizes full production schedule color-coded by Job ID using Plotly Timeline.
Cascade Shift Filters: Enables shop supervisors to filter by Machine -> Month -> ISO Week for granular views.
Export Capabilities: One-click download of production_schedule.csv formatted with exact Start/Finish timestamps for shop management.

## Slide 5
GAP ANALYSIS
Current Code Limitations: Why Whole-Factory Planning Is Needed
1. Single-Machine Routing | Current: Routings specify only 1 machine (e.g. CNC_MILL). --> Impact: Completely ignores parallel machines (CNC_MILL_2..5), artificially causing 4x longer makespans.
2. Zero Material Transit | Current: Transit time between machines is assumed to be 0 mins. --> Impact: Ignores the 15-30 min trolley travel, part washing, and deburring between machine bays.
3. Static Setup Times | Current: Fixed setup hours per item regardless of sequence. --> Impact: Fails to model sequence-dependent changeovers (e.g., lens polisher tooling & fixture swaps).
4. Infinite Buffers | Current: Buffers between machines are assumed infinite (UIS). --> Impact: In reality, buffer racks hold 2-3 carts. If full, upstream machines are physically blocked.
5. Open-Loop Scheduling | Current: Static schedule solved once in batch mode. --> Impact: When a machine fails or an operator is delayed, the schedule shatters with no repair mechanism.

## Slide 6
PART II: TARGET ROADMAP
In-Planning: 4-Layer Cyber-Physical Architecture (ISA-95)
Layer 1: Enterprise Layer (ERP / SCM) — Master Production Schedule (MPS) & Material Requirements (MRP)
Ingests customer purchase orders, committed delivery SLAs, and supplier component lead times.
Layer 2: Advanced Planning & Scheduling (APS) — Global Optimization Engine (PuLP MILP + Master Planning)
Executes finite-capacity planning, decides Make-vs-Buy, and feeds certified promise dates back to ERP.
Layer 3: Practical MES & Reactive Engine — Tri-Controller Coordination (Process, FJSSP, Material Handling)
Process Controller (Chamber batching) + FJSSP Sequencer (Parallel machines) + Cart Staging Coordinator.
Layer 4: Real Shop Floor Execution — Human-in-the-Loop Feedback (Shift Work-Lists & Supervisor Console)
Daily machine dispatch sheets, trolley transfer tickets, and supervisor 1-click disruption repair.

## Slide 7
TARGET ENGINEERING
Phase 1: Flexible Job Shop (FJSSP) & Sequence-Dependent Setups
1. Parallel Machine Routing (FJSSP)
The Available Machine Assets: machine_capacities.csv already lists: • 5 CNC Mills (CNC_MILL_1 to 5) • 5 Lens Polishers (LENS_POLISHER_1 to 5) • 5 Coating Chambers (COATING_CHAMBER_1 to 5) • 5 Assembly Stations (ASSEMBLY_STATION_1 to 5) • 4 Testing Rigs (TESTING_RIG_1 to 4)
Mathematical Formulation: Each operation O_ij can execute on any eligible machine k in M_ij.
CP-SAT Optional Intervals: modeled using AddOptionalIntervalVar with a Boolean presence flag x_ijk, enforcing Sum(x_ijk) == 1.
Impact: Eliminates artificial bottlenecks, balances machine workload, and cuts makespan by 40–60%.
2. Sequence-Dependent Setups (SDST)
Industrial Changeovers: In precision lens & CNC machining, changeover time depends on product family transitions: • Switching optical lens curve requires tool lap change. • Changing milling material (aluminum to titanium) requires chip cleaning and tool offset re-calibration.
Asymmetric Setup Matrix: Matrix S[k, family_A, family_B] defining exact changeover minutes.
CP-SAT Circuit Formulation: Transition times enforced between consecutive tasks on machine k: Start(task_B) >= End(task_A) + S[k, A, B].
Production Clustering: Solver naturally clusters similar items together to minimize total setup downtime across the factory.

## Slide 8
TARGET ENGINEERING
Phase 2: Material Handling & Buffering (Tailored: No AGVs)
Manual Cart / Trolley Inter-Bay Transit
Tailored to Real Factory Reality: Eliminates all unnecessary complexity of autonomous AGV battery curves and robotic LiDAR routing.
Inter-Bay Handling Time (tau_ab): Models the real physical time required to move parts between shop bays: • 0 mins: Consecutive tasks on same machine. • 5–10 mins: Moving within the same department bay. • 15–30 mins: Inter-department move (e.g. CNC Bay -> Optical Polishing -> Vacuum Chamber -> QA Rig).
Physical Work Included: Accounts for washing, burr removal, packing into protective tote bins, and physical trolley wheeling.
Precedence Coupling: Start(Op_j+1) >= End(Op_j) + tau_ab.
Workstation Staging Buffers & Blocking
Finite Intermediate Storage (FIS): Workstations have physical space for only 2–3 tote carts (Capacity C_b).
The Blocking Phenomenon: If machine B's buffer is completely full, upstream machine A cannot release the finished batch. Machine A becomes 'blocked', unable to start its next job.
Aisle Congestion Prevention: Mathematically prevents unmanaged work-in-process (WIP) from piling up in pedestrian and cart corridors.
Cumulative Staging Constraints: Enforced via CP-SAT Cumulative constraints over machine staging areas, keeping shop floor flow lean and organized.

## Slide 9
TARGET ENGINEERING
Phase 3: Upstream Process Batching & Thermal Curing Rules
Optical Coating Chamber Batching
The Batch Process Nature: In COATING_CHAMBER units, running single lenses is economically infeasible due to vacuum cycle & heating overheads.
Lot Sizing Bounds [B_min, B_max]: Enforces minimum chamber fill (e.g. at least 20 units) and maximum chamber volume (e.g. up to 100 units).
Multi-Order Consolidation: Batches lenses from multiple active indents sharing identical optical anti-reflective coating recipes.
Backward Locking: Upstream milling and polishing operations are pulled backward to hit the exact scheduled vacuum pump-down window.
Zero-Wait & Curing Time-Lag Rules
Zero-Wait (ZW) Constraints: For processes where freshly treated optical glass oxidizes or degrades if exposed to ambient air without immediate sealing.
Limited-Wait (LW) Curing Windows: theta_min <= Start(Op_next) - End(Op_batch) <= theta_max.
Physical Cooling & Adhesive Curing: Parts must sit for at least theta_min (e.g., 60 mins cooling after autoclave/chamber) but must enter assembly before adhesive shelf-life theta_max (e.g., 24 hours).
Yield Protection: Eliminates scrap caused by out-of-spec chemical degradation between process stages.

## Slide 10
TARGET ENGINEERING
Phase 4: Human-in-the-Loop Rescheduling (No IoT Needed)
Robust Predictive Buffering
The Brownfield Reality: Machines lack telemetry sensors; schedules cannot be minute-brittle.
Safety Slack Buffers: Adds a 5–10% protective buffer to task runtimes on bottleneck machines.
Variance Absorption: Minor manual delays (machinist adjusting a clamp, 10 min setup slip) are absorbed internally by the safety slack without breaking downstream operations.
Schedule Stability: Prevents 'schedule nervousness' and eliminates constant recalculations during the shift.
Interactive Disruption Console
Supervisor UI in Streamlit: Supervisor logs shop events via simple dropdowns: • Mark Machine Down (e.g. CNC_MILL_2 down until 14:00) • Report Operation Delay (e.g. IOL-OPT-004 delayed 45 min) • Insert Rush Work Order (Priority Military Indent)
Mode 1 — One-Click Right-Shift Repair: Pushes downstream tasks to the right without changing machine assignments or sequence. Zero shop floor confusion!
Mode 2 — Local CP-SAT Re-Optimization: Locks in-progress tasks, re-routes unstarted tasks across active parallel machines (CNC_MILL_1, 3, 4, 5).

## Slide 11
TARGET ENGINEERING
Phase 5: Actionable Shop-Floor Outputs & Dispatch Sheets
1. Machinist Dispatch Sheets
Per-Machine Worklist: Printed or displayed on a tablet at each cell (e.g. CNC_MILL_3).
Clean Sequence Order: Shows exact order of jobs (Job 1 -> Job 2 -> Job 3).
Tooling & Setup Notes: Lists required cutting tools, chuck jaws, and optical fixtures.
Target Time Windows: Displays planned start, planned finish, and customer due date.
2. Material Cart Tickets
Tote Box Traveler Cards: Accompany every physical rolling cart across departments.
Clear Routing Instructions: Informs material handlers: 'Move from CNC Bay to Polishing Bay 2'.
Batch Inspection Sign-off: Includes checkboxes for deburring, ultrasonic washing, and QA count.
Staging Destination: Designates specific input rack buffer at downstream station.
3. Supervisor Dashboard
Live Factory Schedule Gantt: Color-coded multi-machine timeline with setup vs run blocks.
Bottleneck Indicator: Highlights machines running above 85% utilization.
Buffer Congestion Alerts: Flags when a staging buffer exceeds cart capacity.
What-If Simulation: Enables management to test adding a 2nd shift or overtime before committing.

## Slide 12
COMPARATIVE ANALYSIS
Architecture Scorecard: Implemented vs. In-Planning
Factory Scheduling Dimension | Current Implemented State | Target In-Planning System
Machine Allocation | Single fixed machine per operation | Parallel Flexible Job Shop (CNC_MILL_1..5, etc.)
Sequence-Dependent Setups | Static uniform hours per item | SDST transition matrix S[k, A, B] by item family
Shop Floor Material Handling | Assumed 0 minutes instant jump | Manual cart/trolley inter-bay lags (5-30 mins)
Intermediate Buffers | Infinite buffer assumption (UIS) | Finite Intermediate Storage (FIS) with blocking rules
Upstream Process Batching | Ignored; individual piece flow | Vacuum Coating Chamber lot sizing [B_min, B_max]
Shop Floor Uncertainty | Static open-loop batch solver | Safety slack buffers + Supervisor 1-click repair

## Slide 13
PROJECT EXECUTION
Execution Roadmap: Phased Rollout Plan
Phase 1: FJSSP & Parallel Pools [Week 1–2]: Upgrade CP-SAT model to distribute operations across CNC_MILL_1..5 and LENS_POLISHER_1..5; integrate SDST matrix.
Phase 2: Inter-Bay Cart Transit [Week 3]: Integrate transfer times tau_ab (5-30 min) and workstation staging buffer limits C_b to eliminate floor congestion.
Phase 3: Vacuum Chamber Batching [Week 4]: Implement coating chamber batch sizing bounds [B_min, B_max] and Limited-Wait cooling/curing time lags.
Phase 4: Disruption Management [Week 5]: Build the Supervisor Disruption Console in Streamlit for One-Click Right-Shift Repair and Local Re-Optimization.
Phase 5: Floor Dispatch Sheets [Week 6]: Deploy printable and interactive Daily Machine Dispatch Lists and Cart Traveler Tickets for shop floor execution.

## Slide 14
Strategic Impact & Next Steps
1. Proven Solid Foundation: The existing codebase already possesses robust Make-vs-Buy linear programming (PuLP) and baseline CP-SAT scheduling capabilities.
2. Tailored to Manufacturing Reality: By stripping away unrealistic AGV/IoT assumptions, the in-planning system focuses directly on what machinists and supervisors actually need: parallel machine load balancing, setup clustering, cart transit times, and quick repair buttons.
3. High Return on Investment (ROI): Unlocking the 19 parallel machines in your capacity database will immediately slash makespan and backlog without purchasing new machines.
4. Immediate Implementation Action: Proceed to Phase 1: Upgrading CP-SAT to Flexible Job Shop with Parallel Machine Pools in schedule_makespan.py and app.py.